## Slide 1: Options for Difficult Sites
Ben Kele: Managing Director of Arris Pty Ltd

## Slide 2: TradeMutt
Trademutt
  Mental Health Initiative
  Suicide prevention
  https://trademutt.com/

## Slide 3: Arris Pty Ltd
Work Australia wide & Internationally
Mixture of staff with academic and trade skills background
Design, build, operate & maintain water and wastewater treatment & recycling systems
We tend to work on difficult/unusual sites

## Slide 4: Technologies & Techniques
Not tied into any particular method of treating or reusing water
Aim for fit-for-purpose installations
We employ passive/low-input techniques all the way up to RO membranes, ozone disinfection, etc.
We do target robust & reliable treatment and reuse methods
Economic sustainability is just as important as environmental sustainability

## Slide 5: Some Sites are More “Australian” than Others

## Slide 6: Interesting Wildlife at Sites

## Slide 7: Very Good Fishing Spots

## Slide 8: Pacific Islands in Australia
Water Treatment & Water Recycling is progressing
  Australia is a dry continent; so water recycling is popular
Islands often the desire to improve water treatment and recycling is to protect the freshwater lens/aquifer under the island
  This is often the main drinking water supply
Also a strong desire to minimise nutrient runoff to protect the waters surrounding the island
  Especially in the area of the Great Barrier Reef
Looking to get the Whole Community Involved

## Slide 9: Types of Passive & Low Input Systems
Anaerobic treatment
Compost systems
Vermiculture
Soil based treatment systems
Plant based treatment
Constructed wetlands
Sand filters
Mounds (Minnesota)
Woodchip filters
Media & Fabric filters
Dosing Siphons & Flouts
Venturi aeration
Flow past chemical blocks
Treatment chains can be used

## Slide 10: Passive and Low Input Wastewater Systems
A passive wastewater system is a non-mechanical method of treatment
  It typically needs no electricity to operate
A low input wastewater system has minimal mechanical processes
  Frequently it just involves the pumps required to move water through the treatment system
Both passive and low impact systems typically mimic natural processes
Treatment systems, such as constructed wetlands, can be either passive or low input
  It depends on the site

## Slide 11: Who Uses Passive and Low Input Systems?
Used around the world
Popularity has changed over time
There has been a view point that mechanical systems mean more advanced treatment
Assessment of the performance of mechanical systems has questioned that view point
Long term operational costs, both economic and greenhouse gas emissions, of mechanical treatment wastewater systems have also caused people to look for other options

## Slide 12: Scalability
Used from the single household up to municipal sized
Required footprint for the larger volumes can be a limiting factor
  Cost of acquiring the required land
Capital cost can also be a limiting factor
  Buying enough sand media to filter a city is very expensive…
  Some techniques such as constructed wetlands are much more scalable
Europe has been doing larger constructed wetlands and exporting their ideas around the world
  Ecobird https://www.ecobird.fr/
  UFZ: https://www.ufz.de/index.php?en=40551
In Australia constructed wetlands are also being used for larger projects
  Wet Systems: https://wetsystems.com.au/
  Water & Carbon Group: https://waterandcarbon.com.au/

## Slide 13: Low Input can be Large Scale

## Slide 14: Gel Bloc Flocculants & Coagulants
Work at a wide range of pH’s
Cheapest form of Phosphorus removal I’ve encountered
Also reduces total suspended solids
Improves color
Initially designed for mining & stormwater but has wider applications
Easy to retrofit into a treatment chain

## Slide 15: Fat, Oils & Grease
US Standards use lard mixture in a lab at a controlled temperature to test grease-traps, etc
Does not closely resemble what FOG is being encountered in the real world
National Precast Association is currently running a research program on this topic
Contact Ron Naumann
rnaumann@precast.org

## Slide 16: Size Matters in Aeration
Early experiments with aeration mainly failed because of bubble size
Macro-bubble
Micro-bubble
Nano-bubble
All relates to the surface area of the air in the water

## Slide 17: Bubble Size & Surface Area

## Slide 18: Aeration in On-site & Decentralized Wastewater
Mainly installed in ATU’s
Predominately Blowers with aeration discs
  Can be bubble tubing
Tanks typically have an aeration chamber
Servicing the blowers is an important step in the maintenance of these systems

## Slide 19: Aeration Discs

## Slide 21: Low Energy Aeration
Venturi Injectors
Principle discovered in 1797
A venturi injector can be used to put micro-bubbles of air into a pumped water line
Aeration can be achieved without blowers/compressors; just using the power from the pump
Very good at keeping the soil in the dispersal field aerated
Very Good USA manufacturers

## Slide 22: Venturi Aeration

## Slide 23: Aeration in Chambers

## Slide 24: Rhizopod System
Contained Evapotranspiration Trench
Marketed as the Rhizopod System
Developed in Australia
1st installation in 1998
  Tropical Australia
  1st Installation in Temperate Australia 2002
Has a pre-treatment system
Majority are configured as ‘no-release’
  Can also be designed to produce a polished recycled water

## Slide 25: The Rhizopod System

## Slide 26: Rhizopod

## Slide 27: The Rhizopod System

## Slide 28: No Such Magic Place as ‘Away’
In a no-release system some contaminants of concern will accumulate
  Notably salinity
  Sodium salts
  Sodium Adsorption Ratio (SAR)
  Some heavy metals
  Variation in nitrogen & phosphorus
Management is required

## Slide 29: Sodicity
The effect of calcium and sodium ions on soil particles (Asano et al., 2007)

## Slide 30: Sodium Adsorption Ratio (SAR)
The sodium absorption ratio (SAR) is the comparison of the relative preponderance of dissolved sodium (Na+) ions in water to the concentrations of dissolved calcium (Ca2+ ) and magnesium (Mg2+ )
The soil type in the proposed irrigation area is also very important.
  Sodicity has the most impact on heavy clay soils and the least effect on sands

## Slide 31: That’s Odd…
The last research site did not accumulate salinity in the same manner as the other 6 sites
  The SAR also did not rise over time
Treating similar types of wastewater
The last research site had some ‘issues’ and one change was made to the design

## Slide 32: What was Different in the Construction?

## Slide 33: Volcanic Media
Ran a series of bench trials
  Minimum of triplicate
Used different sources of real world high SAR water that had varying salinity
  Trace chemicals
Did single media and dual media trials in different formats
Also tested some non-volcanic media
Looked at major cations, nitrogen and phosphorus, pH, & salinity

## Slide 34: Mixed Ion Exchange and Adsorption Media

## Slide 35: Mixed Media Results
Chart: 
| Qld Zeolite | Black Scoria | Black Scoria + Qld Zeolite | Red Scoria | Red Scoria + Qld Zeolite | Australia Zeolite | Castle Zeolite | Arrow Bore
Average SAR | 6.0847 | 12.0207 | 5.5116 | 34.425 | 24.6399 | 15.2654 | 17.983 | 114.2

## Slide 36
Sample/Analysis | Na mg/L | K mg/L | Mg mg/L | Ca mg/L | SAR | NH4 mg/L
Pump-well | 112.2 | 22.6 | 2.4 | 9.8 | 8.3 | 65.2
Zeolite Tank 1 | 61.3 | 1.1 | 9.9 | 22.3 | 2.7 | 4.9
Zeolite Tank 2 | 59.4 | 1.3 | 11 | 22.9 | 2.6 | 3.8
Pump-well | 120.8 | 22.3 | 2.1 | 8.6 | 9.6 | 69.9
Zeolite Tank 1 | 58.6 | 0.9 | 10.3 | 23.5 | 2.5 | 4.8
Zeolite Tank 2 | 66 | 1.3 | 11.1 | 22.1 | 2.9 | 4.2
Pump-well | 125 | 22.6 | 4.1 | 7.7 | 9.1 | 87.6
Zeolite Tank 1 | 57.6 | 0.9 | 9.8 | 22.6 | 2.5 | 4.9
Zeolite Tank 2 | 63 | 0.9 | 8.4 | 23 | 2.9 | 4.4
Pump-well | 110.4 | 21.9 | 5.5 | 11.3 | 6.7 | 92.6
Zeolite Tank 1 | 61.1 | 1.1 | 9.8 | 22.9 | 2.7 | 4.5
Zeolite Tank 2 | 62.3 | 0.9 | 9 | 21.6 | 2.8 | 4
Pump-well | 119.2 | 21.8 | 4.8 | 8.9 | 8.0 | 74.2
Zeolite Tank 1 | 64.2 | 1.1 | 10.2 | 22.3 | 2.8 | 4.6
Zeolite Tank 2 | 59.8 | 0.8 | 10 | 22.3 | 2.6 | 4.2

## Slide 37: Media May Be Required in Bulk

## Slide 38: Volume and Time Comparison 2017/2018
Chart: 
| Woodford Folk Festival | Planting Festival | Tough Mudder | Rest of the Year
Wastewater Volume kL | 8380 | 617 | 820 | 244
Chart: 
| Woodford Folk Festival | Planting Festival | Tough Mudder | Rest of the Year
Number of Days | 14 | 6 | 6 | 339

## Slide 39: Treatment Chain

## Slide 40: Bamboo Plantation

## Slide 42: Conclusion
Variability in inflow wastewater chemistry, biology, and generation patterns means that treatment systems need to be carefully designed
A ‘one-size fits all’ approach is a common source of failure
Upsizing systems designed to treat domestic wastewater may not be fit-for-purpose
Specialized treatment chains may need to be designed
This does not mean that complex technological solutions are always the answer
A proper design process will detail the:
  Inflow wastewater chemistry & biology
  Wastewater generation pattern
  Availability of suitable operational and maintenance